## Slide 1: Opensource Software class Final Project (Internet Of Things)
Flask Web Server & ESP8266 Board – IOT System
Tae Hwan, Kim
21300210

## Slide 2: Raspberry Pi3 Flask & MQTT Install
Connect with your raspberry pi.
Python package manager pip install.
  sudo apt-get install python-pip
Flask install by using pip
  sudo pip install flask
Install python MQTT module.
  sudo pip install paho-mqtt

## Slide 3: Raspberry Pi3 Flask & MQTT Install
1. MQTT Broker Check
sudo /etc/init.d/mosquitto stop/start/restart/status 2. sudo nano project.py – python file add.
Flask Server
&
MQTT Broker

## Slide 4: Final Project Scenario & Purpose
Publish/Client
Receive result
Publish/Client
Command
<Flask Server, MQTT Broker>
Connect with web
Check Sensor DATA
ESP8266 board 1
Living room
<Led, Door, DHT22, CDS>
ESP8266 board 2
Kitchen
…

## Slide 5: Final Project Scenario & Purpose
Web Server (Smart Phone)
  LED Control
  ESP8266 - Temperature, Humidity, CDS(light sensor) receive
Raspberry Pi3
  Flask Server – Web
  MQTT Broker – Publish/Client (connect with ESP8266 & Web)
  Gateway – Control many ESP8266 (Each Room) simultaneously.
NodeMCU
  LED Toggle
  DHT22 sensor
  CDS(조도센서) sensor
  Door sensor

## Slide 6: ESP8266 board circuit composition
CDS
4.7kΩ
DHT22
GND

## Slide 7: URL Command
LED Control
  http://IP/iot/num/(command)
    led – led Toggle command
    ledon – led ON
    ledoff – led OFF
2. DOOR sensor value Receive
  http://IP/iot/num/DOOR
3. DHT22 value Receive
  http://IP/iot/num/DHT22
4. CDS value Receive
  http://IP/iot/num/CDS

## Slide 8: Check Result (Read Sensor value at web)
<Temperature Check>
IP/iot/(num)/DHT22
<Light Check>
IP/iot/(num)/CDS
<Door Check>
IP/iot/(num)/DOOR